## Slide 1
KAIZEN SHEET
TPM CIRCLE NO :-
TPM CIRCLE NAME :- QM
DEPT :- Aadesh
CELL :- No 4
CELL NAME : CNC Line
ACTIVITY
LOSS NO. / STEP
RESULT AREA
MACHINE / STAGE :- Tapping Machine
OPERATION :- Tapping
KK
QM
PM
JH
SHE
OT
DM
E&T
P
Q
DEF :- A / B / C
C
D
S
M
KAIZEN THEME::- To Eliminate A238 Shaft
Thread Found Not Ok .
IDEA :- Kaizen Drill size change 5.0 mm against to 5.10 mm.
WIDELY/DEEPLY:-
PROBLEM / PRESENT STATUS:- A 238 Shaft
Thread Found Not Ok .
COUNTERMEASURE :- provide 5.0 mm drill
for drilling operation for miner id maintaining
4.95/5.00 mm
BENCHMARK
TARGET
KAIZEN START
KAIZEN FINISH
1
0
08/ 12 /2016
10/2/2017
MANAGER’S SIGN :-
REGISTERED BY :- Bharat k.
REGISTRATION NO&DATE: 08/12/2016
WHY-WHY ANALYSIS :-
RESULT :-
COST INCURRED FOR MAKING KAIZEN
MATERIAL COST
RS.
SCOPE & PLAN FOR HORIZONTAL DEPLOYMENT
LABOUR COST
RS.
TOTAL COST
RS.
SR.
NO.
CELL
TARGET
RESPONSIBILITY
STATUS
A238
Shaft
09/12/2016
BK
completed
ROOT CAUSE :- Due to Blind Hole Tap Not
inserting completely When Tapping Rework
Process.
BEFORE
AFTER
KAIZEN SUSTENANCE
HOW TO DO :- Process audit
FREQUENCY :- As per plan
WHAT TO DO :- PFD , PFMEA CP
To be updated check point added in
Inspection check sheet and PDIR
KAIZEN NO:-
Advik
Team Members :- Bharat , Sayyed.
Benefits:- Prevent re-occurrence of customer complaint, Eliminate in-house rejection ,Mistake proof process generated .
Chart: Threading Rej. Qty
| Dec | Jan | Feb | march
Rejection Qty. | 450 | 0 | 0 | 0
Why1-A 238 Shaft Thread Found not Ok.
Why2-Miner diameter o/s.
Why3- Cnc operation use 5.10 drill for drilling operation.
5.10 mm
5.00 mm