## Slide 1
IDEA – Tool design change
TPM CIRCLE NO :- 01
TPM CIRCLE NAME: Achiever
DEPT :- MACHINE SHOP
CELL:- CBS
CELL NAME:- A247 BKT
ACTIVITY
LOSS NO. / STEP
RESULT AREA
MACHINE / STAGE :- SPM A1/B1
OPERATION :- DRILLING
KK
KAIZEN IDEA SHEET
QM
PM
JH
SHE
OT
DM
E&T
P
Q
A
C
D
S
M
KAIZEN THEME – To Eliminate Id 9.7 Undersize problem in bkt
Problem present status-After changing New tool Observe Undersize or Go gauge Tight
COUNTERMEASURE:- Tool geometry change From End Mill to Hole mill type and size Increase from 9.767 to 9.810mm
BENCHMARK
TARGET
KAIZEN START
TDC
20
0
19/09/2016
TEAM MEMBERS : 1,DYP,SANTOSH.SAKET,NAVNANTH
BENEFITS :-
Defect elimination
MANAGER’S SIGN-D.Y.Pawar.
REGISTERED BY :- Santosh Wakchaure.
REGISTRATION NO. & DATE :
WHY - WHY ANALYSIS :-
Why1 :- Dia9.7 UNDERSIZE.
why2:- Actual Drill size is 9.767mm
Why3 :- Tool size is wrong and geometry is wrong
RESULT :- Dia9.7 Undersize defect eliminated
SCOPE & PLAN FOR HORIZONTAL DEPLOYMENT
SR.
NO.
CELL
TARGET
RESPONSIBILITY
STATUS
KAIZEN SUSTENANCE
WHAT TO DO. Check guard on slide
HOW TO DO:-. Add check point in sheet.
FREQUENCY : Daily.
P15
After
ROOT CAUSE :-Weak tool design
1
KAIZEN FINISH
15/10/16
nil
Before
19/10/2016
DIA 9.7 DRILL-End mill geometry with size 9.767mm size
DIA 9.7 DRILL-Hole mill geometry with size 9.810 mm size
Chart: No. of Defect due TO dia UNDERSIZE
| 42659 | 42690
No. of Defect | 80 | 0