## Slide 1
IDEA :- Cycle Start Button to be Modify.
KAIZEN NO :- 10
TPM CIRCLE NAME: Achiever
DEPT :- MACHINE SHOP
CELL:- Oil pump
CELL NAME:- A262/A107 Rotor
ACTIVITY
LOSS NO. / STEP
RESULT AREA
MACHINE / STAGE :- Press Machine
OPERATION :- Shaft Pressing.
KK
KAIZEN IDEA SHEET
QM
PM
JH
SHE
OT
DM
E&T
P
Q
A,B,C
C
D
S
M
KAIZEN THEME : To Eliminate Accident .
Problem / Present Status :- In A262 Rotor Assembly Operators Finger get Damage while operator enter his hand during running Cycle..
COUNTERMEASURE:-
1.Cycle Start Button to be Modify as till operation will complete operator need to keep Pressing Cy. Start Button. If Hand removed from button cycle is Reset & Cylinder goes up.
BENCHMARK
TARGET
KAIZEN START
TDC
Minor Accident
Zero Accident
05.04.2016
06.04.2016
TEAM MEMBERS : 1.Ramesh Thanvi ,Yuvraj Desai.
BENEFITS :-
1 Accident Chance Eliminate.
MANAGER’S SIGN :- D. Y. Pawar
REGISTERED BY :- Ramesh Thanvi
REGISTRATION NO. & DATE : 06.04.2016
WHY - WHY ANALYSIS :-
Why1 :- In A262 Rotor Assembly Operators Finger get Damage.
Why2:- Operator enter his hand during running Cycle.
Why3 :- Once Cy. Start button Press, Operator can Remove His Hand & engage in Other activity.
Why4 :- Current weak Design Concept of Cy. Start Button.
RESULT :-
Accident Chance Eliminate.
Safe For Operator.
SCOPE & PLAN FOR HORIZONTAL DEPLOYMENT
SR.
NO.
CELL
TARGET
RESPONSIBILITY
STATUS
KAIZEN SUSTENANCE
WHAT TO DO:- Cy. Start button Verify in start of Sheet.
HOW TO DO:- Point to be Added in JH Sheet.
P15
ROOT CAUSE : Current weak Design of Cy. Start Button.
1
Complete
KAIZEN FINISH
D.C
20.5.16
Yuvraj Desai
After