## Slide 1: Quality Tools
Problem Solving

## Slide 2: Quality Control Tools
    Pareto chart
    Histogram
    Process flow diagram
    Check sheet
    Scatter diagram
    Control chart
      Run chart
    Cause and effect diagram

## Slide 3: Pareto Principle
Vilfredo Pareto (1848-1923) Italian economist
  20% of the population has 80% of the wealth
Juran used the term “vital few, trivial many”. He noted that 20% of the quality problems caused 80% of the dollar loss.
7 Quality Tools

## Slide 4: Pareto chart
7 Quality Tools
% Complaints

## Slide 5: Pareto Chart
Percent from each cause
Causes of poor quality
Machine calibrations
Defective parts
Wrong dimensions
Poor Design
Operator errors
Defective materials
Surface abrasions
0
10
20
30
40
50
60
70
(64)
(13)
(10)
(6)
(3)
(2)
(2)
Notes: Pareto analysis uses an ordered histogram to highlight the major causes of quality problems.

## Slide 6: Histogram
7 Quality Tools

## Slide 7: Histogram
0
5
10
15
20
25
30
35
40
1 2 6 13 10 16 19 17 12 16 20 17 13 5 6 2 1
Notes: Histograms are graphical frequency tables that visually capture and display the variation in a set of data.

## Slide 8: Flowcharts
Flowcharts
  Graphical description of how work is done.
  Used to describe processes that are to be improved.
7 Quality Tools

## Slide 9: Flow Diagrams
" Draw a flowchart for whatever you do. Until you do, you do not know what you are doing, you just have a job.”
    -- Dr. W. Edwards Deming.

## Slide 10: Flowchart
Activity
Decision
Yes
No
7 Quality Tools

## Slide 11: Flowchart
Notes: A flowchart diagrams the steps in a process. Flowcharts help problem solvers better understand the process so they can highlight quality problems.

## Slide 12: Flow Diagrams

## Slide 13: Flow Diagrams

## Slide 14: Process Chart Symbols
Operations
Inspection
Transportation
Delay
Storage

## Slide 15: Process Chart
Step
Operation
Transport
Inspect
Delay
Storage
Distance
(feet)
Time
(min)
Description
of
process
1
2
3
4
5
6
7
8
9
10
11
Unload apples from truck
Move to inspection station
Weigh, inspect, sort
Move to storage
Wait until needed
Move to peeler
Apples peeled and cored
Soak in water until needed
Place in conveyor
Move to mixing area
Weigh, inspect, sort
Total
Page 1 0f 3
480
30
5
20
15
360
30
20
190 ft
20 ft
20 ft
50 ft
100 ft
Date: 9-30-00
Analyst: TLR
Location: Graves Mountain
Process: Apple Sauce

## Slide 17: Check Sheet
  
   

  
 
  
  
 

Shifts
Defect Type
7 Quality Tools
   

## Slide 18: Check Sheet
COMPONENTS REPLACED BY LAB
TIME PERIOD: 22 Feb to 27 Feb 1998
REPAIR TECHNICIAN: Bob
TV SET MODEL 1013
Integrated Circuits ||||
Capacitors |||| |||| |||| |||| |||| ||
Resistors ||
Transformers ||||
Commands
CRT |
Notes: A check sheet is a fact-finding tool used to collect data about quality problems. A typical check sheet tallies the number of defects by previously identified categories. The next step is to graph the defects per category in a histogram.

## Slide 19: Cause-and-Effect Diagrams
Show the relationships between a problem and its possible causes.
Developed by Kaoru Ishikawa (1953)
Also known as …
  Fishbone diagrams
  Ishikawa diagrams
7 Quality Tools

## Slide 20: Cause and Effect “Skeleton”
Quality
Problem
Materials
Equipment
People
Procedures
7 Quality Tools

## Slide 21: Fishbone Diagram
Quality
Problem
Machines
Measurement
Human
Process
Environment
Materials
Faulty testing equipment
Incorrect specifications
Improper methods
Poor supervision
Lack of concentration
Inadequate training
Out of adjustment
Tooling problems
Old / worn
Defective from vendor
Not to specifications
Material-
handling problems
Deficiencies
in product design
Ineffective quality
management
Poor process design
Inaccurate
temperature
control
Dust and Dirt
Notes: A cause-and-effect diagram, or fishbone diagram, is a chart showing the different categories of problem causes.

## Slide 22: Cause and effect diagrams
Advantages
  making the diagram is educational in itself
  diagram demonstrates knowledge of problem solving team
  diagram results in active searches for causes
  diagram is a guide for data collection

## Slide 23: Cause and effect diagrams
To construct the skeleton, remember:
For manufacturing - the 4 M’s
  man, method, machine, material
For service applications
  equipment, policies, procedures, people

## Slide 24: Scatter Diagram
.
Notes: Scatter diagrams and tightness of points plotted on the graph gives an indication of the strength of the relationship. A cluster of points resembling a straight line indicates the strongest correlation between the variables. In this graph, there is a strong positive correlation between x and y.

## Slide 25: Run Charts
Run Charts (time series plot)
  Examine the behavior of a variable over time.
  Basis for Control Charts

## Slide 26: Control Chart
18
12
6
3
9
15
21
24
27
2
4
6
8
10
12
14
16
Sample number
Number of defects
UCL = 23.35
LCL = 1.99
c = 12.67
Notes: Process control involves monitoring a production process and charting the results on a control chart. If any of the points plotted falls outside the control limits, the process is out-of-control.

## Slide 27
Control Charts
7 Quality Tools

## Slide 28: “Stem and leaf” displays
Data
Integrated Circuit Response Time (ps)

## Slide 29: “Stem and leaf” displays
3 7 4 4 7 7 4 3 7 9
4 6 0 1 5 6 2 6 7 1 1 5 6 4 8 3 4
5 6 1
6 0 0
Integrated Circuit Response Time (ps)

## Slide 30: Dot diagrams
3
4
5
6
Plant A
Plant B
Integrated Circuit Response Time (ps)